To remove the curb climber on a Dolomite walker

- Remove the center hubcap using a screwdriver or small flat blade. This exposes the nut for the axle bolt.

- Remove this nut and slide the bolt enough to remove the curb climber. Re-thread bolt through the fork.

- Replace the nut and tighten securely.

- Tap the hubcap in place.