# Clarke Health Care Product, Inc

7830 Steubenville Pike

Oakdale PA 15071-9226

(724) 695-2122

# Installing Curb Climber

- Remove hub caps, use pliers to pull off.

- Remove axle bolt and nut

- Insert curb climber, on inside of walker right wheel, position between wheel and fork. The top hole is for 8” casters (Futura) and bottom hole for 7” casters (Opal 2000).

- Reinsert bolt and tighten nut

- Replace hub caps, using a rubber mallet.